## Slide 1: GIS and Spatial Analytics
Lecture 6

## Slide 2: What Will We Cover Today?
Buffers Recap!
Points, Near (Closest) and Distances
Summary Statistics
Geocoding Addresses

## Slide 3: Spatial Overlays
Spatially combine two layers to:
  Generate a new output data layer
  Assign attributes of one data layer to another
  Usually one of the data layers will be polygons
    A point-in-polygon overlay is typical

## Slide 4: Proximity Tools
Buffer
Multiple Ring Buffer
Near
Point Distance

## Slide 6: Buffers for Lines and Polygons
Move circle of specified radius along line
(or lines forming polygon)

## Slide 7: Multiple Ring Buffer
Creates a new feature class of buffer features using a set of buffer distances. The new features may be dissolved using the distance values or as a set of individual features.

## Slide 8: Near
Computes the distance from each point in a feature class to the nearest line or point in another feature class.

## Slide 9: GIS is not perfect
A GIS cannot perfectly represent the world for many reasons, including:
The world is too complex and detailed.
We make decisions (how to categorize data, how to define zones or districts) that are not always fully informed or justified.
It is impossible to make a perfect representation of the world, so uncertainty is inevitable
Uncertainty degrades the quality of a spatial representation

## Slide 10: A Conceptual View of Uncertainty
Real World
Conception
Data conversion and Analysis
Measurement &
Representation
Result
error propagation
Notes: U1:
1. Spatial uncertainty. firstly, Tobler’s law: spatial autocorrelation, secondly, natural units of analysis: what is the measurement unit for a soil profile, how might we delimit an environmental impact of spillage from an oil tanker?
(In nature, ecological phenomena or discrete
features either influence neighbors, are influenced by neighbors, or both. The level of
neighbor influence may vary with distance and other factors, making the autocorrelation
function non-linear. In general, the closer the neighbors, the greater the level of
correlation, which distorts statistical tests of significance in analyses such as correlation,
regression, or analysis of variance (Cliff and Ord 1981).
)
2. Vagueness. can exist both in the positions of the boundaries of a zone and its attributes. how many oak trees in a forested zone can label as oak woodland? how far from ABQ to Socorro
3. Ambiguity. many objects are assigned different labels by different national or cultural groups. this is inherently ambiguous. second, imperfect indicators of phenomena cause ambiguous. For example, detail household income figures, provide direct indicator of demand for goods and services; rates of multiple car ownership might provide indirect indicator for household income data.
U2:
1. Measurement & Representation
objects and fields: raster and vector are characterized by different uncertainties: vector requires a priori conceptualization of the nature and extent of geographic individuals and the ways in which they nest together into higher-order zones. raster defines square or rectangle cells, with boundaries that bear no relationship at all to natural features. furthermore, the measurement process can actually introduce uncertainty.
2. error and accuracy
Digitizing error, GPS accuracy
U3:

## Slide 11: Response to Uncertainty
Acknowledge it!
Use metadata to document the uncertainty
Analysis can sometimes identify the impact of input uncertainty on output
Use multiple sources of data
Be honest and appropriately modest in reporting the results of analysis

## Slide 12: Common Errors
One-to-many, vs. one-to-one joins
Intend a one-to-one join
  Result is a one-to-many join
Be careful with islands
  Every polygon in a shapefile gets a record, even if it belongs to the same unit

## Slide 13: Single Parts vs. Multiple Parts
If there are islands, a unit (state, province) must be drawn as a multi-part feature in the shapefile (the spatial data)
Then there will be only one row in the attribute table
If each island is drawn as a separate feature, there will be multiple rows in the attribute table

## Slide 14: Multi-Part vs. Single-Part
Note the population
sum is wrong here
We join the state population figures to
a file of states, here to a multi-part
shapefile

## Slide 15: Merge and Single-to-Multi-part Commands
Merge – takes single-part features and merges to multi-part
Explode – goes from multi- to single, making the parts of multi-part features independent
These work on all features in a layer rather than just selected features when used via the geoprocessing tools in QGIS

## Slide 16: Spatial is special: 3 critical concepts
  Distance/Proximity
  Adjacency
  or neighborhood
  Interaction

## Slide 17: Fundamental Spatial Concepts
Distance
  The magnitude of spatial separation
  Euclidean (straight line) distance often only an approximation
Adjacency or neighborhood
  Nominal or binary (0,1) equivalent of distance
  Levels of adjacency exist: 1st, 2nd, 3rd nearest neighbor, etc..
Interaction
  The strength of the relationship between entities
  An inverse function of distance

## Slide 18: Statistics Tools
Frequency
Summary Statistics

## Slide 19: Frequency
Produces a list of the unique code occurrences and their frequency in an output table for a specified set of fields from an input feature class or table.
Optionally, summary items may be totaled for each unique code combination—for example, the total area for unique combinations of zoning and land use.

## Slide 20: Summary Statistics
Generates summary statistics for fields from an input table or feature class and saves them in an output table.
This tool contains the following statistics types: sum, mean, minimum, maximum, standard deviation, range, first value, and last value.

## Slide 21: The Process of Geocoding:
Standardizing the address
Searching for potential candidates
Scoring each candidate
Matching address to best candidate

## Slide 22: Standardizing the Address
During this step the address is broken into components
For example: street number, street name, street type and street direction

## Slide 23: Matching Address to Best Candidate
The geocoding service looks for the potential candidate with the highest score
If the score exceeds the minimum match score setting, then the service matches the address with that candidate

## Slide 24: Geocoding Process Settings
Spelling Sensitivity
Minimum Candidate Score
Minimum Match Score

## Slide 25: MMQGIS PLUGIN

## Slide 26: ADDRESSES